## Slide 1: IoT Security
Levente Buttyán
CrySyS Lab, BME
www.crysys.hu

## Slide 2: Internet of Things (IoT)
Smart Home
Wearables
Smart City
Intelligent Transport
Connected Car
Smart Retail
Supply Chain Automation
Precision Agriculture
Industry 4.0
Digital Healthcare
Embedded computers connected to the Internet …

## Slide 3: IoT (in)security

## Slide 4: Indeed...

## Slide 5: Compromising IoT devices
Main attack surfaces
  Some embedded IoT devices are connected directly to the Internet
  Many embedded IoT devices have wireless interfaces (e.g., WiFi, Bluetooth, ZigBee, ...)
  Some IoT devices may be unattended and physically accessible
Common weaknesses
  Insecure ports are open unnecessarily
  Password based authentication with weak passwords
  Exploitable vulnerabilities in the software running on the device
  Software updates are not available (at all or in a timely manner)
  No protection against physical attacks
shodan.io

## Slide 6: Example: Insecure ports and weak passwords

## Slide 7: Example: Unpatched vulnerabilities

## Slide 8: IoT devices seem to be the weakest link

## Slide 9: IoT from a hacker’s perspective
Internet of Things
cheap (in every sense)
computers easy to compromise
now easily searchable and
accessible remotely

## Slide 12: Explanation by security economics
vendors build
cheap devices
maximize profit
minimize time to market
more features, no security
consumers buy
cheap devices
optimize price/value ratio
don’t understand the risk
can’t identify quality
misplaced incentives
makes no sense to build secure, but more expensive devices
lemon market:
information asymmetry
consumers will pay average price
quality vendors leave the market

## Slide 13: European Cyber Resilience Act
Published on September 15, 2022 (very fresh!)
Aims at setting common cybersecurity standards for connected devices and services in order to protect consumers and the market from cyber incidents (such as Mirai)
Introduces rules to protect digital products (including IoT devices) that are not covered by any previous regulation (e.g., NIS)  it will be the first IoT security legislation in the world!
Sets minimum security requirements for connected devices, both during product development and throughout the product life cycle
Make manufacturers responsible for ensuring that their products are digitally secure
Enables consumers to have better information regarding the security of their devices

## Slide 14: European Cyber Resilience Act (cont’d)
Two product categories: critical and non-critical
  compliance of critical products (e.g., VPNs, routers, firewalls, operating systems) will be assessed by third-parties
  non-critical products (90% of the market) will only require a self-declaration of conformity
Proposed requirements include:
  providing an “appropriate” level of cybersecurity (risk-based approach)
  prohibition to sell products with any known vulnerability
  regular tests to identify vulnerabilities
  security by default configuration
  limitation of attack surfaces
  minimization of incident impact
Member States must put in place market surveillance bodies
Penalties for non-complying with the requirements can amount to €15 million or 2.5% of the annual turnover

## Slide 15: IoT malware

## Slide 16: Why infecting IoT devices?
It’s technically possible
  IoT devices are (re)programmable --» they can run (malicious) code
It makes sense economically
  Number of IoT devices is huge and still growing
  IoT devices are almost always on and connected
  IoT devices are valuable targets
  IoT devices are not so esoteric (as you might think)
  Many deployed IoT devices were not designed with security in mind
  Many deployed IoT devices are not operated with security in mind
  Vulnerable devices are easy to find (e.g., with shodan.io)
  Device compromise is hard to detect
Notes: Getting value for low cost:
number of IoT devices is huge and still growing
IoT devices are almost always on and connected (routers, web cameras)
IoT devices are valuable targets (interesting data, non-negligible computing power, stepping stone towards some internal network infrastructure)
IoT devices are not so esoteric (they often run some embedded Linux)
IoT devices are not (yet) designed with security in mind (open ports, easy-to-guess passwords, old and vulnerable software, no patching, …)
IoT devices are not operated with security in mind (ports left open, default passwords not changed, firmware never updated, logs never examined, …)
vulnerable devices are easy to find (shodan.io, censys.io)
device compromise is hard to detect (no visible signs, no anti-virus scanners)

## Slide 17: Example: Mirai botnet
On 21st October 2016
  Dyn experienced a DDoS attack on their managed DNS servers
  The attack was launched by ~100 000 Internet enabled IoT devices, all infected by the Mirai malware
  According to some experts, the attack magnitude reached 1.2 Tbps
On 27th November 2016
  A large number of Deutsche Telekom customers using Speedport home routers reported connectivity problems
  The root cause of the problem was found to be a new variant of Mirai which was trying to expand the botnet

## Slide 18: Example: Mirai botnet (cont’d)
Targeted devices were DVRs, IP cameras, routers, and printers
Number of IoT devices infected:
  65 000 in the first 20 hours of the outbreak
  200-300 000 in steady state (and a peak of 600 000)
Source code published  rapid emergence of new features
  improved infection capabilities
  DGA in place of a hardcoded C&C domains
  obfusctaing binaries to slow down reverse engineering efforts
Operation:

## Slide 19: Potential consequences
If IoT devices are compromised in large quantity by malware, they can be organized into IoT botnets (attack infrastructure)
Compromised IoT devices can steal confidential data and cause privacy breaches
Compromised IoT devices in cyber-physical systems may cause physical damage or fatal accidents

## Slide 20: SETIT project
Goal:
  Develop new methods (algorithms, protocols, tools, …) that enhance the security of IoT systems
Research areas:
  Software security for embedded devices
    bug prediction by static code analysis
  Platform security for embedded devices
    secure boot and remote firmware update
    malware detection and attestation of malware free state
  Algebraic foundations and cryptographic building blocks
Consortium:
(2018-1.2.1-NKP-2018-00004)

## Slide 21: The challenge of IoT malware detection
Anti-virus (AV) products currently available for desktop PCs
  do not support IoT devices
  have too demanding system requirements
IoT devices have resource constraints
  computing power, storage space, connectivity / network bandwidth
Existing proposals have limitations
  Network-based solutions
    detection is performed on a gateway device in front of the IoT device
    can be circumvented with encrypted traffic or USB pendrives
  Cloud-based solutions
    samples are sent to the cloud for analysis and detection
    delayed decision
    needs constant network availability

## Slide 22: We proposed…
SIMBIoTA = SIMilarity Based IoT Anti-virus*
SIMBIoTA-ML = SIMBIoTA with Machine Learning**
Efficient – affordable for resource constrained IoT devices
  Small storage requirements
  Lightweight detection process
Effective – they actually work!
  Very high (90-98%) true positive detection rate, even for previously unseen samples!
  Very low (0-1%) false positive rate
* Cs. Tamás, D. Papp, L. Buttyán, SIMBIoTA: Similarity-Based Malware Detection on IoT Devices, 6th International Conference on Internet of Things, Big Data and Security (IoTBDS), 2021.
** D. Papp, G. Ács, R. Nagy, L. Buttyán, SIMBIoTA-ML: Light-weight, Machine Learning-based Malware
Detection for Embedded IoT Devices, 7th International Conference on Internet of Things, Big Data
and Security (IoTBDS), 2022. (Best Paper Award)

## Slide 23: Operation of SIMBIoTA
Malware
intelligence network
Honeypot farms
Malware feeds
Public malware
repositories
Malware
database
Malware
similarity
graph +
dominating
set
TLSH values of
the nodes in the
dominating set
Binary file
Malware detector
process
IoT device
Backend

## Slide 24: Operation of SIMBIoTA-ML
Malware
intelligence network
Honeypot farms
Malware feeds
Public malware
repositories
Malware
database
Machine
learning
Binary file
Malware detector
process
IoT device
Backend
Benign
database
Trained
ML model
TLSH
values
TLSH
values

## Slide 25: More ingredients for securing IoT devices
System hardening
  No open ports, no weak passwords
  Switch on available OS configuration settings for increased security
  Disable JTAG access
Strong authentication (cryptography based, multi-factor)
Cryptographic protection for data in transit and data at rest
Malware protection (and attestation of malware-free state)
  Detection of malicious files
  Continuous integrity monitoring of the device
Verified boot process
Trusted Execution Environment (TEE)
Secure (remote) software update

## Slide 26: Acknowledgements
The presented work was carried out within the SETIT Project, which has been implemented with the support provided from the National Research, Development and Innovation Fund of Hungary, financed under the 2018-1.2.1-NKP funding scheme (project no. 2018-1.2.1-NKP-2018-00004).
The presented work was also supported by the Ministry of Innovation and Technology NRDI Office within the framework of the Artificial Intelligence National Laboratory Program (RRF-2.3.1-21-2022-00004).